## Slide 1
Enrico Schiassi
Systems and Industrial Engineering
The University of Arizona, USA
Doctoral Final Oral Defense
November 30th 2022
Extreme Theory of Functional Connections (X-TFC)
for Problems Involving Differential Equations with Applications to Optimal Control Problems
Prof. Roberto Furfaro (advisor, chair)
Prof. Jianqiang Cheng (member)
Prof. Larry Head (member)
Prof. Clayton T. Morrison (member)

## Slide 2: Contents
Section I
  Overview and Opportunity
  State-of-the-art Differential Equation solvers
  Neural Networks for Differential Equations
  Novelty and contribution
Section II
  X-TFC for Initial Values ODEs
  X-TFC for Two Point Boundary Value ODEs
  X-TFC for bivariate PDEs
  X-TFC for Optimal Control Problems
  Estimate on the generalization error
Section III
  Results and discussions
Section IV
  Published works
  Works in progress and future works

## Slide 3
Section I

## Slide 4: Overview & Opportunity
  Many real-world problems are modeled via Differential Equations (DEs)
    Physics, engineering, finance, biology, chemistry, oceanography, epidemiology, etc.
  There is the need to have accurate, efficient, robust, and reliable tools to solve problems involving DEs
    Forward problems
      The goal is to find the function that solves the DEs
    Inverse problems
      The goal is to estimate the parameters governing the DEs

## Slide 5: Overview & Opportunity (cont’d)
The research goal is to develop and test an efficient, robust, reliable, and unified framework to tackle forward and inverse problems governed by Differential Equations

## Slide 6: State-of-the-art Differential Equations solvers
ODEs: Euler’s Method, Euler’s Modified Method, Runge-Kutta Second Order Method, Runge-Kutta Fourth Order Method, Milne’s Predictor-Corrector Method
PDEs: Finite Difference Method (FDM), Finite Element Method (FEM), Finite Volume Method (FVM)
Need to be modified and/or coupled with other methods for inverse problems

## Slide 7: Neural Networks for Differential Equations
General single PDE
Data-set (experimental and/or synthetic)
NN approximation of the DE unknown solution
Physics-driven training
Data-driven training
Data-physics-driven training for forward problems
Data-physics-driven training for inverse problems
~1990
2019
Physics-Informed Neural Network
Neural Network
Physics-Informed Neural Network

## Slide 8: Physics-Informed Neural Networks
Data
Physics-Informed Neural Networks (PINN)
Data-physics-driven solution of DEs
Neural Networks
Physics Laws
Data-physics-driven DE parameters discovery
Physics-driven solution of DEs
Forward Problems
Inverse Problems

## Slide 9: Classic PINN
Main limitations
Gradient based methods are employed to train the network
  Cost effective
  Complexity of the networks can cause divergence
  Linear problems treated as nonlinear problems
Initial and/or Boundary Conditions (e.g., DE constraints) included in the loss function
  Cost effective (especially for PDEs)
  Presence of competing objectives in the loss function
    Gradient pathologies causing the training failure in learning the DE constraints
    Introduction of additional hyperparameters*
Gradient-based
methods
Image from: Lu, L., Meng, X., Mao, Z. and Karniadakis, G.E., 2021. DeepXDE: A deep learning library for solving differential equations. SIAM Review, 63(1), pp.208-228.
* Wang, S., Teng, Y. and Perdikaris, P., 2021. Understanding and mitigating gradient flow pathologies in physics-informed neural networks. SIAM Journal on Scientific Computing, 43(5), pp.A3055-A3081.
Vancouver
Raissi, M., Perdikaris, P. and Karniadakis, G.E., 2019. Physics-informed neural networks: A deep learning framework for solving forward and inverse problems involving nonlinear partial differential equations. Journal of Computational physics, 378, pp.686-707.

## Slide 10: X-TFC*
x
x
(or analytically)
Least-Squares
* Extreme Theory of Functional Connections
Main limitations
Gradient based methods are employed to train the network
  Cost effective
  Complexity of the networks can cause divergence
  Linear problems treated as nonlinear problems
Initial and/or Boundary Conditions (e.g., DE constraints) included in the loss function
  Cost effective (especially for PDEs)
  Presence of competing objectives in the loss function
    Gradient pathologies causing the training failure in learning the DE constraints
    Introduction of additional hyperparameters
Schiassi, E., Furfaro, R., Leake, C., De Florio, M., Johnston, H. and Mortari, D., 2021. Extreme theory of functional connections: A fast physics-informed neural network method for solving ordinary and partial differential equations. Neurocomputing, 457, pp.334-356.

## Slide 11: Novelty and contribution
X-TFC* conceptualization and development
  ELM** and TFC*** are brought together for the first time to form an efficient, robust, reliable, and unified framework to tackle forward and inverse problems governed by Differential Equations - Schiassi et al. 2021
X-TFC application to a variety of real-world problems
  Nuclear reactor dynamics (forward problem) - Schiassi et al. 2022
  Optimal control problems for general and aerospace applications (forward problem) - Schiassi et al. 2022
  Epidemiological compartmental model parameters estimation (inverse problem) - Schiassi et al. 2021
Estimate on the X-TFC generalization error for solving forward problems
  General ODEs - Schiassi et al. 2022/2023
  Two Points Boundary Value Problems (TPBVPs) for optimal control problems solved via indirect method - Schiassi et al. 2022/2023
  Hamilton Jacobi Bellman (HJB) equation for optimal control problems with integral quadratic cost - Schiassi et al. 2022
* Schiassi, E., Furfaro, R., Leake, C., De Florio, M., Johnston, H. and Mortari, D., 2021. Extreme theory of functional connections: A fast physics-informed neural network method for solving ordinary and partial differential equations. Neurocomputing, 457, pp.334-356.
*** Mortari, D., 2017. The theory of connections: Connecting points. Mathematics, 5(4), p.57.
** Huang, G.B., Zhu, Q.Y. and Siew, C.K., 2006. Extreme learning machine: theory and applications. Neurocomputing, 70(1-3), pp.489-501.

## Slide 12
Section II

## Slide 13: X-TFC for Initial Value ODEs
Original constrained IVP
1) Constrained Expression
2) Unconstrained IVP
3) Residual to be minimized
4) Trained the Network via Least-Squares => *

## Slide 14: X-TFC for Two Point Boundary Value ODEs
Original constrained TPBVP
1) Constrained Expression
2) Unconstrained TPBVP
3) Residual to be minimized
4) Trained the Network via Least-Squares => *

## Slide 15: X-TFC for bivariate PDEs
Original constrained bivariate PDEs
1) Constrained Expression
2) Unconstrained PDEs
3) Residual to be minimized
4) Trained the Network via iterative Least-Squares => *

## Slide 16: X-TFC for Optimal Control Problems (cont’d)
Optimal Control Problems (OCPs) are generally hard and computationally expensive.
  Open-Loop solutions
  Closed-Loop Solutions
In general, Open-Loop solutions can be found in two ways
  Direct Method: Transform a continuous problem in a finite NLP problem and find the minimum
  Indirect Method: Apply Pontryagin Minimum Principle (PMP) to derive the necessary conditions for optimality
    The solution of the OCP reduces to the solution of a Two Point Boundary Value Problem (TPBVP) that is a system of first order ODEs

## Slide 17: X-TFC for Optimal Control Problems (cont’d)
Learn the solutions via X-TFC
OCP
TPBVP
Apply PMP
Schiassi, E., D’Ambrosio, A., Furfaro, R., Pontryagin Neural Networks for the Class of Optimal Control Problems with Integral quadratic cost, to be submitted

## Slide 18: X-TFC for Optimal Control Problems
Optimal Control Problems (OCPs) are generally hard and computationally expensive.
  Open-Loop solutions
  Closed-Loop Solutions
In general, Closed-Loop solutions are found via solving the HJB equation
  HJB equation guarantees a necessary and sufficient condition for the optimality
  The HJB equation is a nonlinear PDE
  The space complexity of HJB equations is exponential with respect to the number of dimensions of the system (generally d>3 for space applications)
    Curse of dimensionality => traditional numerical methods to solve PDE, such as FEM, becomes impracticable

## Slide 19: X-TFC for Optimal Control Problems (cont’d)
Learn V(t,x) via X-TFC
OCP
HJB PDE II
Value Function
Optimal Control
HJB PDE I
Finite Horizon Problem
Schiassi, E., D'Ambrosio, A. and Furfaro, R., 2022. Bellman Neural Networks for the Class of Optimal Control Problems With Integral Quadratic Cost. IEEE Transactions on Artificial Intelligence.

## Slide 20: X-TFC for Optimal Control Problems (cont’d)
Infinite Horizon Problem
Learn V(x) via X-TFC
OCP
HJB PDE II
Value Function
Optimal Control
HJB PDE I
Schiassi, E., D'Ambrosio, A. and Furfaro, R., 2022. Bellman Neural Networks for the Class of Optimal Control Problems With Integral Quadratic Cost. IEEE Transactions on Artificial Intelligence.

## Slide 21: Estimate on the generalization error
Generic system of Differential Equations
Initial Conditions
Boundary Conditions
Residuals
Generalization Error
Training Error
Generalization Error Bound

## Slide 22
Section III

## Slide 23: Section III outline
X-TFC for benchmarks ODEs and PDEs
X-TFC for Nuclear Reactor Dynamics
X-TFC for Optimal Control Problems
  Open-loop solutions
  Closed-loop solutions
X-TFC for Epidemiological Compartmental Models

## Slide 24: X-TFC for benchmarks ODEs and PDEs
  Activation Function: Hyperbolic Tangent
  Input Weights and Biased sampled from: unif [-3,3]
Schiassi, E., De Florio, M., D’Ambrosio, A., Furfaro, R., Estimates on the generalization error of X-TFC in learning ODE solutions, to be submitted
Generalization Error Bound

## Slide 25: X-TFC for benchmarks ODEs and PDEs (cont’d)
Schiassi, E., De Florio, M., D’Ambrosio, A., Furfaro, R., Estimates on the generalization error of X-TFC in learning ODE solutions, to be submitted
  Activation Function: Hyperbolic Tangent
  Input Weights and Biased sampled from: unif [-3,3]
Generalization Error Bound

## Slide 26: X-TFC for benchmarks ODEs and PDEs (cont’d)
  Activation Function: Hyperbolic Tangent
  Input Weights and Biased sampled from: unif [-3,3]
Generalization Error Bound

## Slide 27: X-TFC for benchmarks ODEs and PDEs (cont’d)
Schiassi, E., Furfaro, R., Leake, C., De Florio, M., Johnston, H. and Mortari, D., 2021. Extreme theory of functional connections: A fast physics-informed neural network method for solving ordinary and partial differential equations. Neurocomputing, 457, pp.334-356.
Hyperparameters
Activation Function: Hyperbolic Tangent
Number of Points per variable: 30
Number of Neurons: 150-170
Input Weights and Biased sampled from: unif [-1,1]
  X-TFC Computational Time: ~ 8.1 [ms]
  X-TFC Computational Time: ~ 9.3 [ms]
  X-TFC Computational Time: ~ 22.5 [ms] – 10 iterations

## Slide 28: X-TFC for Nuclear Reactor Dynamics
Test Case 1: Step Reactivity Insertion in Thermal Reactor
Test Case 2: Ramp Reactivity Insertion
Test Case 3: Sinusoidal Reactivity
Test Case 4: Reactivity as a Function of the Neutron Density
Test Case 5: Temperature Feedback Reactivity
Test Case 6: Thermal Hydraulics Feedback
Schiassi, E., De Florio, M., Ganapol, B.D., Picca, P. and Furfaro, R., 2022. Physics-informed neural networks for the point kinetics equations for nuclear reactor dynamics. Annals of Nuclear Energy, 167, p.108833. Vancouver

## Slide 29: X-TFC for Nuclear Reactor Dynamics (cont’d)
Time-domain decomposition scheme
System of IVPs
Decomposition into n time steps
Constrained expression
Condition for continuity
Systems of m DEs

## Slide 30: X-TFC for Nuclear Reactor Dynamics (cont’d)
Test Case 1: Step Reactivity Insertion in Thermal Reactor

## Slide 31: X-TFC for Nuclear Reactor Dynamics (cont’d)
Test Case 6: Thermal Hydraulics Feedback

## Slide 32: X-TFC for Nuclear Reactor Dynamics (cont’d)

## Slide 33: X-TFC for Nuclear Reactor Dynamics (cont’d)

## Slide 34: X-TFC for Nuclear Reactor Dynamics (cont’d)

## Slide 35: X-TFC for Optimal Control Problems
Learn the solutions via X-TFC
PMP
OCP – Linear Feldbaum Problem
TPBVP
Schiassi, E., D’Ambrosio, A., Furfaro, R., Pontryagin Neural Networks for the Class of Optimal Control Problems with Integral quadratic cost, to be submitted

## Slide 36: X-TFC for Optimal Control Problems (cont’d)
Hyperparameters
100 equally distributed training points
Hyperbolic tangent as activation function
Adam Optimizer with learning rate 0.001 for PINN
Inputs and bias sampled from U(-3;3) for PIELM and X-TFC
Schiassi, E., D’Ambrosio, A., Scorsoglio, A., Furfaro, R. and Curti, F., CLASS OF OPTIMAL SPACE GUIDANCE PROBLEMS SOLVED VIA INDIRECT METHODS AND PHYSICS-INFORMED NEURAL NETWORKS, 31st AAS/AIAA Space Flight Mechanics Meeting, Virtual, February 1-4, 2021

## Slide 37: X-TFC for Optimal Control Problems (cont’d)
Schiassi, E., D’Ambrosio, A., Furfaro, R., Pontryagin Neural Networks for the Class of Optimal Control Problems with Integral quadratic cost, to be submitted

## Slide 38: X-TFC for Optimal Control Problems (cont’d)
The minimum time 2D orbit transfer OCP is posed as following:
Applying the PMP the TPBVP (plus transversality condition) that we will solve via X-TFC is:
where x1, x2, and x3 are radial distance from the Sun, radial velocity, and tangential velocity respectively; and:
s.t.
Schiassi, E., D’Ambrosio, A., Drozd, K., Curti, F. and Furfaro, R., 2022. Physics-Informed Neural Networks for Optimal Planar Orbit Transfers. Journal of Spacecraft and Rockets, pp.1-16.

## Slide 39: X-TFC for Optimal Control Problems (cont’d)
The CEs and their derivatives are:
The unknowns and the losses are:
Mapping coefficient from t in [t0; tf] to z in [z0; zf]
The β’s are called switching functions
The h are the SLNNs that are trained via ELM, where 𝛏’s are the output weights of the network

## Slide 40: X-TFC for Optimal Control Problems (cont’d)
Performances analysis
Activation Function: Logistic
Input weights and bias sampled from: unif [-1,1]
We compare our results with GPOPS. The results obtained with GPOPS were the following: tf = 3.3194, H(tf) + 𝚪 = 6.5 x 10-3, with a CPU time ~ 30 [s]

## Slide 41: X-TFC for Optimal Control Problems (cont’d)
Time evolution of the states and control
Optimal Trajectories
Activation Function: Logistic
Input weights and bias sampled from: unif [-1,1]
N = 50, L = 20
L2 = 4.5 x 10-3

## Slide 42: X-TFC for Optimal Control Problems (cont’d)
Learn V(t,x) via X-TFC
OCP
HJB PDE II
Optimal Control
HJB PDE I
Schiassi, E., D'Ambrosio, A. and Furfaro, R., 2022. Bellman Neural Networks for the Class of Optimal Control Problems With Integral Quadratic Cost. IEEE Transactions on Artificial Intelligence.

## Slide 43: X-TFC for Optimal Control Problems (cont’d)
Hyperparameters
4900 (equally distributed, and randomly distributed) training points
  Plus 1000 training points on the boundary for PINN
Hyperbolic tangent as activation function
Adam Optimizer with learning rate 0.001 for PINN
LBFGS Optimizer for Deep-TFC

## Slide 44: X-TFC for Optimal Control Problems (cont’d)
Optimal Control
Value Function

## Slide 45: X-TFC for Optimal Control Problems (cont’d)
Learn V(x) via X-TFC
OCP
Optimal Control
HJB PDE

## Slide 46: X-TFC for Optimal Control Problems (cont’d)
Hyperparameters
4900 (equally distributed, and randomly distributed) training points
  Plus one training points on the boundary for PINN
Hyperbolic tangent as activation function
Adam Optimizer with learning rate 0.001 for PINN
LBFGS Optimizer for Deep-TFC

## Slide 47: X-TFC for Optimal Control Problems (cont’d)
Optimal Control
Value Function

## Slide 48: X-TFC for Epidemiological Compartmental Models
Schiassi, E., De Florio, M., D’Ambrosio, A., Mortari, D. and Furfaro, R., 2021. Physics-informed neural networks and functional interpolation for data-driven parameters discovery of epidemiological compartmental models. Mathematics, 9(17), p.2069.
  Compartmental Epidemiological Model, Susceptible-Infectious-Recovered (SIR) :
  Constraints:
  Known Parameters: birth rate and natural death rate (considered equal to keep a constant population), µ
  CE:
  Unknown Parameters:
    Infectious rate,
    Recovery rate gamma,
    Basic Reproduction Number (expected number of secondary cases produced by a single infections),
  Where the total number of population is

## Slide 49: X-TFC for Epidemiological Compartmental Models (cont’d)
  Activation Function: ArcTan
  Number of Points : 100
  Number of Neurons: 50
  Input Weights and Bias sampled from: unif [-10,10]
  Data Perturbation: unif[-1,1]*noise
  Birth and Mortality rate: 0.1000
  Exact Infectious rate: 0.5000
  Exact Recovery rate: 0.3333
  Exact Basic Reproduction Number : 1.5000
  IC: S(0) = 100, I(0) = 50, R(0) = 0
  Time span: 15 days
  noise = 5

## Slide 50: X-TFC for Epidemiological Compartmental Models (cont’d)
  Activation Function: ArcTan
  Number of Neurons: 100
  Input Weights and Biased sampled from: unif [-10,10]
  Noise: 0
  Activation Function: ArcTan
  Number of Points: 100
  Input Weights and Biased sampled from: unif [-10,10]
  Noise: 0

## Slide 51: X-TFC for Epidemiological Compartmental Models (cont’d)
  Activation Function: ArcTan
  Number of Neurons: 100
  Input Weights and Biased sampled from: unif [-10,10]
  Noise: 5
  Activation Function: ArcTan
  Number of Points: 100
  Input Weights and Biased sampled from: unif [-10,10]
  Noise: 5

## Slide 52
Section IV

## Slide 53: Conclusions
ELM and TFC are brought together for the fist time to form X-TFC
  Efficient, robust, reliable, and unified framework to tackle forward and inverse problems governed by DE
  Overcomes the main issues of the state-of-the-art DE solvers
  Overcomes the main issues of the state-of-the-art PINN frameworks
X-TFC has been applied to a wide variety of engineering problems
  Nuclear reactor dynamics
  Optimal control problems for general and aerospace applications
  Epidemiological compartmental models

## Slide 54: Works in progress and future works
X-TFC adaptation for problem with sharp gradients/discontinuities
  Domain decomposition for TBPVP - in progress
  Domain decomposition for PDEs - future
X-TFC for closed-loop solution of OCPs
  Application to satellite attitude - in progress
  From software to hardware – future
Unmodelled dynamics quantification - future

## Slide 55: Other Projects
Schiassi, E., Furfaro, R., Kargel, J.S., Watson, C.S., Shugar, D.H. and Haritashya, U.K., 2019. GLAM Bio-Lith RT: A Tool for Remote Sensing Reflectance Simulation and Water Components Concentration Retrieval in Glacial Lakes. Frontiers in Earth Science, 7, p.267.
Code available publicly at: https://github.com/nsidc/HMA_GLAM_BioLith-RT_5
Assessing the changes in hydrology and cryosphere in the High Mountain Asia region, by leading the development of a remote sensing software for glacier lakes characterization ( GLAM-BioLithRT ) within the NASA HiMAT project.

## Slide 56: Other Projects (cont’d)
Software for Asteroid Binary Systems characterization via light-curves inversion, in collaboration with NASA and Planetary Science Institute (PSI).

## Slide 57: Other Projects (cont’d)
NASA Near Earth Objects Surveillance Mission (NEOSM):
  Part of the Target Follow-Up working Group, led by Prof. Roberto Furfaro
  Developing an intelligent system for decision-making related to Near-Earth Objects (NEOs) follow-up strategies and crating a medium-fidelity NEOs simulator to support and validate the ranking system and the decision making tool

## Slide 58: Journal publications
Schiassi, E., D'Ambrosio, A. and Furfaro, R., 2022. Bellman Neural Networks for the Class of Optimal Control Problems With Integral Quadratic Cost. IEEE Transactions on Artificial Intelligence.
De Florio, M., Schiassi, E. and Furfaro, R., 2022. Physics-informed neural networks and functional interpolation for stiff chemical kinetics. Chaos: An Interdisciplinary Journal of Nonlinear Science, 32(6), p.063107.
De Florio, M., Schiassi, E., Ganapol, B.D. and Furfaro, R., 2022. Physics-Informed Neural Networks for rarefied-gas dynamics: Poiseuille flow in the BGK approximation. Zeitschrift für angewandte Mathematik und Physik, 73(3), pp.1-18.
D’Ambrosio, A., Schiassi, E., Johnston, H., Curti, F., Mortari, D. and Furfaro, R., 2022. Time-energy optimal landing on planetary bodies via theory of functional connections. Advances in Space Research, 69(12), pp.4198-4220.
Schiassi, E., D’Ambrosio, A., Drozd, K., Curti, F. and Furfaro, R., 2022. Physics-informed neural networks for optimal planar orbit transfers. Journal of Spacecraft and Rockets, 59(3), pp.834-849.
Schiassi, E., De Florio, M., Ganapol, B.D., Picca, P. and Furfaro, R., 2022. Physics-informed neural networks for the point kinetics equations for nuclear reactor dynamics. Annals of Nuclear Energy, 167, p.108833.
De Florio, M., Schiassi, E., D’Ambrosio, A., Mortari, D. and Furfaro, R., 2021. Theory of functional connections applied to linear odes subject to integral constraints and linear ordinary integro-differential equations. Mathematical and Computational Applications, 26(3), p.65.
Schiassi, E., De Florio, M., D’ambrosio, A., Mortari, D. and Furfaro, R., 2021. Physics-informed neural networks and functional interpolation for data-driven parameters discovery of epidemiological compartmental models. Mathematics, 9(17), p.2069.
Schiassi, E., Furfaro, R., Leake, C., De Florio, M., Johnston, H. and Mortari, D., 2021. Extreme theory of functional connections: A fast physics-informed neural network method for solving ordinary and partial differential equations. Neurocomputing, 457, pp.334-356.
De Florio, M., Schiassi, E., Ganapol, B.D. and Furfaro, R., 2021. Physics-informed neural networks for rarefied-gas dynamics: Thermal creep flow in the Bhatnagar–Gross–Krook approximation. Physics of Fluids, 33(4), p.047110.
D’ambrosio, A., Schiassi, E., Curti, F. and Furfaro, R., 2021. Pontryagin neural networks with functional interpolation for optimal intercept problems. Mathematics, 9(9), p.996.
Drozd, K., Furfaro, R., Schiassi, E., Johnston, H. and Mortari, D., 2021. Energy-optimal trajectory problems in relative motion solved via Theory of Functional Connections. Acta Astronautica, 182, pp.361-382.
De Florio, M., Schiassi, E., Furfaro, R., Ganapol, B.D. and Mostacci, D., 2021. Solutions of Chandrasekhar’s basic problem in radiative transfer via theory of functional connections. Journal of Quantitative Spectroscopy and Radiative Transfer, 259, p.107384.
Johnston, H., Schiassi, E., Furfaro, R. and Mortari, D., 2020. Fuel-efficient powered descent guidance on large planetary bodies via theory of functional connections. The journal of the astronautical sciences, 67(4), pp.1521-1552.
Watson, C.S., Kargel, J.S., Shugar, D.H., Haritashya, U.K., Schiassi, E. and Furfaro, R., 2020. Mass loss from calving in Himalayan proglacial lakes. Frontiers in Earth Science, 7, p.342.
Bishop, M.P., Young, B.W., Colby, J.D., Furfaro, R., Schiassi, E. and Chi, Z., 2019. Theoretical evaluation of anisotropic reflectance correction approaches for addressing multi-scale topographic effects on the radiation-transfer cascade in mountain environments. Remote Sensing, 11(23), p.2728.
Schiassi, E., Furfaro, R., Kargel, J.S., Watson, C.S., Shugar, D.H. and Haritashya, U.K., 2019. GLAM Bio-Lith RT: A Tool for Remote Sensing Reflectance Simulation and Water Components Concentration Retrieval in Glacial Lakes. Frontiers in Earth Science, 7, p.267.
Schiassi, E., Furfaro, R. and Mostacci, D., 2016. Bayesian inversion of coupled radiative and heat transfer models for asteroid regoliths and lakes. Radiation Effects and Defects in Solids, 171(9-10), pp.736-745.

## Slide 59: Conferences and preprints
Schiassi, E., D’Ambrosio, A., and Furfaro, R., 2022. An Overview of X-TFC Applications for Aerospace Optimal Control Problems. In 2nd International Conference on Applied Intelligence and Informatics 2022 (AII2022), Reggio Calabria (Italy), 2022
Furfaro, R., D'Ambrosio, A., Schiassi, E. and Scorsoglio, A., 2022. Physics-Informed Neural Networks for Closed-Loop Guidance and Control in Aerospace Systems. In AIAA SCITECH 2022 Forum (p. 0361).
D’Ambrosio, A., Schiassi, E., Curti, F. and Furfaro, R., 2021. Physics-Informed Neural Networks Applied to a Series of Constrained Space Guidance Problems. In 31st AAS/AIAA Space Flight Mechanics Meeting.
D’Ambrosio, A., Schiassi, E., Curti, F. and Furfaro, R., PHYSICS-INFORMED NEURAL NETWORKS FOR OPTIMAL PROXIMITY MANEUVERS WITH COLLISION AVOIDANCE AROUND ASTEROIDS.
Schiassi, E., D’Ambrosio, A., Scorsoglio, A., Furfaro, R. and Curti, F., 2021. Class of optimal space guidance problems solved via indirect methods and physics-informed neural networks.
Schiassi, E., D’Ambrosio, A., Furfaro, R. and Curti, F., PHYSICS-INFORMED NEURAL NETWORKS FOR OPTIMAL INTERCEPT PROBLEM.
Schiassi, E., D'Ambrosio, A., De Florio, M., Furfaro, R. and Curti, F., 2020. Physics-informed extreme theory of functional connections applied to data-driven parameters discovery of epidemiological compartmental models. arXiv preprint arXiv:2008.05554.
Schiassi, E., D’ambrosio, A., Johnston, H., De Florio, M., Drozd, K., Furfaro, R., Curti, F. and Mortari, D., 2020, August. Physics-informed extreme theory of functional connections applied to optimal orbit transfer. In Proceedings of the AAS/AIAA Astrodynamics Specialist Conference, Lake Tahoe, CA, USA (pp. 9-13).
Schiassi, E., D’Ambrosio, A., Johnston, H., Furfaro, R., Curti, F. and Mortari, D., 2020, August. Complete energy optimal landing on small and large planetary bodies via theory of functional connections. In Proceedings of the Astrodynamics Specialist Conference, AAS, South Lake Tahoe, CA, USA (pp. 9-12).
Schiassi, E., Leake, C., De Florio, M., Johnston, H., Furfaro, R. and Mortari, D., 2020. Extreme theory of functional connections: A physics-informed neural network method for solving parametric differential equations. arXiv preprint arXiv:2005.10632.
Schiassi, E., Furfaro, R., Johnston, H. and Mortari, D., 2020. Fuel-efficient powered descent guidance on planetary bodies via theory of functional connections 1: Solution of the equations of motion. In AAS/AIAA Astrodynamics Specialist Conference, 2019 (pp. 275-290). Univelt Inc..
Schiassi, E., X-TFC: A Physics-Informed Neural Network Framework For Solving Forward and Inverse Problems Involving Parametric Differential Equations, 1st World Online Conference on Theory of Functional Connections May 22nd 2020 (presentation)
Schiassi, E., Physics-Informed Extreme Theory of Functional Connections for Parametric ODEs and PDEs, Los Alamos-Arizona days, May 18th-19th 2020 (presentation).

## Slide 60: Citations and h-index
  18 peer reviewed journal articles and 13 conference papers/preprints
  309 citations with an h-index of 11, as reported by Google Scholar
  141 citations with an h-index of 8, as reported by Scopus
  143 citations with an h-index of 7, as reported by Web of Science

## Slide 61: Reviewer for
Physic of Fluid – AIP Publishing
Scientific Reports – Springernature
Advances in Space Research – Elsevier
Engineering Structures - Elsevier
Frontier Physics - Frontiers

## Slide 62: Awards
Best Paper Awards “ An Overview of X-TFC Applications for Aerospace Optimal Control Problems” at the 2nd International Conference on Applied Intelligence and Informatics 2022 (AII2022), Reggio Calabria (Italy), 2022.

## Slide 63: Acknowledgments
Advisor and Lab Director: Prof. Roberto Furfaro
Postdoc: Dr. Lorenzo Federici
Ph.D. Candidate: Mario De Florio
Ph.D. Students: Tanner Campell, Kristofer Drozd, Luca Ghilardi, Andrea Scorsoglio
Research Engineer: Brian Gaudet
Visiting Researchers: Dr. Andrea D’Ambrosio, Dr. Paolo Picca, Mattia Pugliatti, Laura Laghi
Space Systems Engineering Laboratory

## Slide 64: Acknowledgments (cont’d)
Prof. Fabio Curti, The University of Arizona
Dr. Andrea D’Ambrosio, MIT
Mario De Florio, The University of Arizona
Kristofer Drozd, The University of Arizona
Prof. Barry Ganapol, The University of Arizona
Dr. Jeffrey S Kargel, Planetary Science Institute
Dr. Byong Kwon, The University of Arizona
Dr. Hunter Johnston, Texas A&M/Aerospace Corporation
Dr. Carl Leake, Texas A&M/JPL
Tyler Linder, University of North Dakota
Prof. Daniele Mortari, Texas A&M
Prof. Domiziano Mostacci, University of Bologna
Dr. Paolo Picca, The University of Arizona
Coauthors and collaborators
Ph.D. Committee
Prof. Roberto Furfaro (advisor, chair)
Prof. Larry Head (member)
Prof. Jianqiang Cheng (member)
Prof. Clayton T. Morrison (member)
SIE Department
Cindy Nguyen
Prof. Jianqiang Cheng
Prof. Larry Head

## Slide 65
Thanks for your attention
https://ssel.arizona.edu/person/enrico-schiassi

## Slide 66
Backup Slides

## Slide 67: Overview & Opportunity
In mathematics, a Differential Equation (DE) is an equation that links one or several unknown functions and their derivatives
In applications, the functions usually are physical quantities, the derivatives are their rates of change. The DE defines a relationship among them
  In classical mechanics, the motion of a body is described by its position (unknown function), velocity (first derivative), and acceleration (second derivative), as the time varies
In many real-world applications, a closed-form expression for the DE solution is not available.
  The solutions are approximated via numerical methods
https://en.wikipedia.org/wiki/Classical_mechanics
Zill, D.G., 2012. A first course in differential equations with modeling applications. Cengage Learning.

## Slide 68: Overview & Opportunity (cont’d)
Point Kinetics Equations for nuclear reactor dynamics
Initial Conditions
Schiassi, E., De Florio, M., Ganapol, B.D., Picca, P. and Furfaro, R., 2022. Physics-informed neural networks for the point kinetics equations for nuclear reactor dynamics. Annals of Nuclear Energy, 167, p.108833. Vancouver

## Slide 69: Overview & Opportunity (cont’d)
Optimal Control Problem for planar orbit transfer
Schiassi, E., D’Ambrosio, A., Drozd, K., Curti, F. and Furfaro, R., 2022. Physics-Informed Neural Networks for Optimal Planar Orbit Transfers. Journal of Spacecraft and Rockets, pp.1-16.

## Slide 70: Overview & Opportunity (cont’d)
Epidemiological compartmental model for virus spread
Initial Conditions
Schiassi, E., De Florio, M., D’Ambrosio, A., Mortari, D. and Furfaro, R., 2021. Physics-informed neural networks and functional interpolation for data-driven parameters discovery of epidemiological compartmental models. Mathematics, 9(17), p.2069.

## Slide 71: Neural Networks for data-regression
Shallow Single Input Single Output NN
Classic Neural Networks (NN)
(Non)linear map
Given data-set
Extreme Learning Machines (ELM)
Huang, G.B., Zhu, Q.Y. and Siew, C.K., 2006. Extreme learning machine: theory and applications. Neurocomputing, 70(1-3), pp.489-501.

## Slide 72: Data-driven training
Classic Neural Networks (NN)
(Non)linear map
Given data-set
Extreme Learning Machines (ELM)
Damped Harmonic Oscillator
https://benmoseley.blog/my-research/so-what-is-a-physics-informed-neural-network/

## Slide 73: Data-physics-driven training
Given data-set
Neural
Networks
Physics-Informed Neural Network
https://benmoseley.blog/my-research/so-what-is-a-physics-informed-neural-network/
Damped Harmonic Oscillator

## Slide 74: PIELM*
Least-squares
(or analytically)
* Physics-Informed Extreme Learning Machine
Main limitations
Gradient based methods are employed to train the network
  Cost effective
  Complexity of the networks can cause divergence
  Linear problems treated as nonlinear problems
Initial and/or Boundary Conditions (e.g., DE constraints) included in the loss function
  Cost effective (especially for PDEs)
  Presence of competing objectives in the loss function
    Gradient pathologies causing the training failure in learning the DE constraints
    Introduction of additional hyperparameters
Dwivedi, V. and Srinivasan, B., 2020. Physics informed extreme learning machine (pielm)–a rapid method for the numerical solution of partial differential equations. Neurocomputing, 391, pp.96-118.

## Slide 75: Deep-TFC*
x
x
Gradient-based
methods
g(x)
* Deep Theory of Functional Connections
Main limitations
Gradient based methods are employed to train the network
  Cost effective
  Complexity of the networks can cause divergence
  Linear problems treated as nonlinear problems
Initial and/or Boundary Conditions (e.g., DE constraints) included in the loss function
  Cost effective (especially for PDEs)
  Presence of competing objectives in the loss function
    Gradient pathologies causing the training failure in learning the DE constraints
    Introduction of additional hyperparameters
Leake, C. and Mortari, D., 2020. Deep theory of functional connections: A new method for estimating the solutions of partial differential equations. Machine learning and knowledge extraction, 2(1), pp.37-55.
Mortari, D., 2017. The theory of connections: Connecting points. Mathematics, 5(4), p.57.

## Slide 76: PINN Frameworks

## Slide 77: TFC versus PINNs for DEs
  The Theory of Functional Connections (TFC) [Mortari, 2017] is a mathematical framework for functional interpolation
    The function is approximated via a constrained expression
      Sum of a free-chosen function and a functional that analytically satisfies the constraints
    TFC is applied to solve parametric DEs
      The free-chosen function is an expansion of orthogonal polynomials (Chebyshev or Legendre)
      The constraints are the Initial/Boundary Conditions (IC or BC)
  The Physics-Informed (PI) Neural Networks (NN) Methods are a “novel” approach, coming from the Machine Learning community
    The DE unknown solutions are approximated via a (Deep) Neural Network (NN), and the DEs drive the NN training
Schiassi, E., X-TFC: A Physics-Informed Neural Network Framework For Solving Forward and Inverse Problems Involving Parametric Differential Equations, 1st World Online Conference on Theory of Functional Connections May 22nd 2020 (presentation)

## Slide 78: X-TFC for nonlinear ODE
Schiassi, E., X-TFC: A Physics-Informed Neural Network Framework For Solving Forward and Inverse Problems Involving Parametric Differential Equations, 1st World Online Conference on Theory of Functional Connections May 22nd 2020 (presentation)

## Slide 79: X-TFC for nonlinear ODE (cont’d)
Schiassi, E., X-TFC: A Physics-Informed Neural Network Framework For Solving Forward and Inverse Problems Involving Parametric Differential Equations, 1st World Online Conference on Theory of Functional Connections May 22nd 2020 (presentation)

## Slide 80: X-TFC for nonlinear ODE (cont’d)
Schiassi, E., X-TFC: A Physics-Informed Neural Network Framework For Solving Forward and Inverse Problems Involving Parametric Differential Equations, 1st World Online Conference on Theory of Functional Connections May 22nd 2020 (presentation)

## Slide 81: X-TFC for nonlinear ODE (cont’d)
Schiassi, E., X-TFC: A Physics-Informed Neural Network Framework For Solving Forward and Inverse Problems Involving Parametric Differential Equations, 1st World Online Conference on Theory of Functional Connections May 22nd 2020 (presentation)

## Slide 82: HJB-based GNC architecture
Schiassi, E., D'Ambrosio, A. and Furfaro, R., 2022. Bellman Neural Networks for the Class of Optimal Control Problems With Integral Quadratic Cost. IEEE Transactions on Artificial Intelligence.

## Slide 83: Estimates on the generalization error of classic PINNs for learning DE solutions (forward problems)
In the classic PINNs (and the variants) the DE residuals are collocated at training points
  DEs residual are minimized at the training points
In the presence on discontinuities in the solutions, residuals are measures that do not make sense pointwise
  The generalization error estimate points out the limitations of a PINN for approximating discontinuous solutions
Domain Decomposition
Techniques
ISSUE
POSSIBLE SOLUTION
Mishra, S. and Molinaro, R., 2022. Estimates on the generalization error of physics-informed neural networks for approximating PDEs. IMA Journal of Numerical Analysis.

## Slide 84: Understanding and Mitigating Gradient Flow Pathologies in PINNs
Wang, S., Teng, Y. and Perdikaris, P., 2021. Understanding and mitigating gradient flow pathologies in physics-informed neural networks. SIAM Journal on Scientific Computing, 43(5), pp.A3055-A3081.
Vancouver
Loss
Unbalanced gradients
Stiff gradient flow dynamics

## Slide 85: Gaussian Processes vs Neural Networks
Gaussian Process (GPs) are non-parametric regressors while Neural Networks (NNs) are parametric regressors
  With GPs you have to carry your data all the times as you need to condition on the data
GPs are not scalable to big dataset while NNs are scalable
  With GPs you have to invert a large covariance matrix with all the data
  With NNs you can use mini-batches
GPs quantify the uncertainty in their predication while NNs do not
GPs automatically balance the tradeoff of data-fit and model complexity
  NNs can over fit
    Regularization techniques are needed

## Slide 86: X-TFC vs SVM-TFC*
* Leake, C., Johnston, H., Smith, L. and Mortari, D., 2019. Analytically embedding differential equation constraints into least squares support vector machines using the theory of functional connections. Machine learning and knowledge extraction, 1(4), pp.1058-1083.
X-TFC
SVM-TFC

## Slide 87: X-TFC vs SVM-TFC (cont’d)
X-TFC
SVM-TFC

## Slide 88: Adaptive Moment Estimation (ADAM) Optimizer
Kingma, D.P. and Ba, J., 2014. Adam: A method for stochastic optimization. arXiv preprint arXiv:1412.6980
1st moment:
2nd moment:

## Slide 89: Section III comp. exam outline
1D steady advection-diffusion equation
Optimal control problems: open-loop solutions
  Linear Feldbaum problem
  Energy optimal rendezvous
  Time-energy optimal intercept
Optimal control problems: closed-loop solutions
  Finite horizon problem with linear dynamics and quadratic cost
  Infinite horizon problem with linear dynamics and quadratic cost

## Slide 90: 1D Steady Advection-Diffusion
1D
Linear
Steady-state (e.g., time independent)
Sharpness of the solution increase with
Hyperparameters
TPBVP

## Slide 91: 1D Steady Advection-Diffusion (cont’d)

## Slide 92: 1D Steady Advection-Diffusion (cont’d)

## Slide 93: 1D Steady Advection-Diffusion (cont’d)

## Slide 94: 1D Steady Advection-Diffusion (cont’d)

## Slide 95: 1D Steady Advection-Diffusion (cont’d)

## Slide 96: Energy Optimal Rendezvous
Learn the solutions via X-TFC
PMP
OCP
TPBVP
Schiassi, E., D’Ambrosio, A., Scorsoglio, A., Furfaro, R. and Curti, F., CLASS OF OPTIMAL SPACE GUIDANCE PROBLEMS SOLVED VIA INDIRECT METHODS AND PHYSICS-INFORMED NEURAL NETWORKS, 31st AAS/AIAA Space Flight Mechanics Meeting, Virtual, February 1-4, 2021

## Slide 97: Energy Optimal Rendezvous (cont’d)
Hyperparameters
20 equally distributed training points
80 neurons
Hyperbolic tangent as activation function
Inputs and bias sampled from U(-3;3)
Schiassi, E., D’Ambrosio, A., Scorsoglio, A., Furfaro, R. and Curti, F., CLASS OF OPTIMAL SPACE GUIDANCE PROBLEMS SOLVED VIA INDIRECT METHODS AND PHYSICS-INFORMED NEURAL NETWORKS, 31st AAS/AIAA Space Flight Mechanics Meeting, Virtual, February 1-4, 2021

## Slide 98: Time-Energy Optimal Intercept
s.t.
PMP
Learn the solutions via X-TFC
Schiassi, E., D’Ambrosio, A., Furfaro, R. and Curti, F., PHYSICS-INFORMED NEURAL NETWORKS FOR OPTIMAL INTERCEPT PROBLEM, IAA/AAS SciTech Forum 2020, Dec. 08-10, 2020, Moscow, Russia
OCP
TPBVP

## Slide 99: Time-Energy Optimal Intercept (cont’d)
Performances analysis (=1)
Activation Function: hyperbolic tangent
Input weights and bias sampled from: U [-1,1]
We compare our results with GPOPS II. The results obtained with GPOPS II were the following: tf = 45.54, H(tf) + 𝚪 = 2.35 x 10-6, with a CPU time ~ 1.48 [s]
r0 = [500, -600, -500] m
v0 = [-50, 60, 5] m/s
aT = [1, -2, 0,1] m/s2 (assumed constant)
Schiassi, E., D’Ambrosio, A., Furfaro, R. and Curti, F., PHYSICS-INFORMED NEURAL NETWORKS FOR OPTIMAL INTERCEPT PROBLEM, IAA/AAS SciTech Forum 2020, Dec. 08-10, 2020, Moscow, Russia

## Slide 100: Time-Energy Optimal Intercept (cont’d)
Time evolution of the states and control
Optimal Trajectories
Activation Function: hyperbolic tangent
Input weights and bias sampled from: unif [-1,1]
Number of points: 20
Number of neurons: 16
Schiassi, E., D’Ambrosio, A., Furfaro, R. and Curti, F., PHYSICS-INFORMED NEURAL NETWORKS FOR OPTIMAL INTERCEPT PROBLEM, IAA/AAS SciTech Forum 2020, Dec. 08-10, 2020, Moscow, Russia

## Slide 101: Finite Horizon Problem with Linear Dynamics and Quadratic Cost
Learn V(t,x) via X-TFC
OCP
HJB PDE II
Optimal Control
HJB PDE I
Schiassi, E., D’Ambrosio, A., and Furfaro, R. Bellman Neural Networks for the Class of Optimal Control Problems with quadratic cost, in preparation

## Slide 102: Test Case 2: Ramp Reactivity Insertion

## Slide 103: Test Case 3: Sinusoidal Reactivity

## Slide 104: Test Case 4: Reactivity as a Function of the Neutron Density

## Slide 105: Test Case 5: Temperature Feedback Reactivity

## Slide 106: Estimate on the Generalization Error for IVP

## Slide 107: Estimate on the Generalization Error for IVP (cont’d)

## Slide 108: Estimate on the Generalization Error for 2nd order TPBVP

## Slide 109: Estimate on the Generalization Error for TPBVP arising from the PMP application to OCP

## Slide 110: Estimate on the Generalization Error for TPBVP arising from the PMP application to OCP (cont’d)

## Slide 111: Estimate on the Generalization Error for TPBVP arising from the PMP application to OCP (cont’d)

## Slide 112: Estimate on the Generalization Error for TPBVP arising from the PMP application to OCP (cont’d)

## Slide 113: Estimate on the Generalization Error for TPBVP arising from the PMP application to OCP (cont’d)